## Slide 1: DiSCNet: A Dual-Branch CNN for Bearing Fault Diagnosis
R E S E A R C H P A P E R R E V I E W
Paper summary, methodological analysis, and open questions for discussion
Presented by Animesh | Mechanical Engineering
Lab Research Discussion

## Slide 2
P A R T O N E
Paper Summary
Motivation, methodology, architecture, and reported results

## Slide 3: Motivation & the Shift in Methodology
B ACKG ROUN D
The goal: machine failure prediction aims to reduce downtime and ensure operational safety, as manual inspection is not reliable.
TRADITIONAL MODELS
Handcrafted Features
– Rely on human-engineered features and standard signal processing
– Generalize well across conditions
– Cannot model complex, non-linear relationships in the data
DEEP LEARNING MODELS
Data-Driven (CNNs)
Part 1 — Paper Summary
– Automatically extract hierarchical features from raw signals
– Offer high diagnostic precision
– Act as black boxes; prone to overfitting on specific datasets

## Slide 4: Overcoming 1D Limits with STFT and CWT
S I G N AL REP RES EN T AT I ON
The problem: in raw 1D time-domain signals, transient micro-spalls are easily masked by large amounts of sinusoidal background noise.
Part 1 — Paper Summary
 | STFT | CWT
Full name | Short-Time Fourier Transform | Continuous Wavelet Transform
Resolution | Fixed time-frequency resolution | Multi-resolution — wavelet compresses / stretches
Strength | Captures stable harmonic content well | Localizes non-stationary, transient features well
Weakness | Rigid window struggles with fast transient impacts | Higher computational cost per transform

## Slide 5: The DiSCNet Approach & Novelty
MET HODOLOG Y
01
Transfer Learning
Pre-trained ResNet-50 models (originally optimized on ImageNet) act as feature extractors for the mechanical vibration data.
02
Weighted Fusion
STFT and CWT features are merged with a learnable weighted fusion mechanism, instead of simple concatenation, to dynamically prioritize each
branch.
03
End-to-End Optimization
The model trains using the Adam optimizer and Cross-Entropy loss, redistributing network weights specifically for fault detection.
04
Part 1 — Paper Summary
The Novelty
DiSCNet is benchmarked against other lightweight models — balancing diagnostic accuracy while reducing parameter count and FLOPs.

## Slide 6: Data Pre-processing & Input Representation
MET HODOLOG Y
STEP 1
Signal Slicing
Continuous vibration signals segmented into 1024-sample windows (0.2 s at 5120 Hz).
→
STEP 2
Windowing
256-sample Hann window slides across the 1024 samples with 50% overlap (128 samples) to localize frequencies without artificial noise.
→
STEP 3
Image Conversion
Resulting matrices are normalized, mapped with a Jet color map, resized to 224 × 224, and converted to 3-channel RGB images.
Part 1 — Paper Summary
Input to network: 1024 samples per window → 224 × 224 × 3 image tensor, per branch (STFT and CWT)

## Slide 7: Dual-Branch Architecture & Latent Space Extraction
ARCHI T ECT UR E
STFT image → ResNet-50 backbone (compact)
CWT image → ResNet-50 backbone (compact)
Global Average Pooling (GAP)
Part 1 — Paper Summary
Compact backbones: redundant deep layers (Stage 4) were physically removed from each ResNet-50 to reduce computation.
Latent space extraction: GAP flattens each 3D convolutional map into a 1024-dimensional feature descriptor — the embedding vector representing the vibration
signal's coordinates in the model's abstract latent space.

## Slide 8: Feature Fusion & Classification Head
ARCHI T ECT UR E
Bottleneck Compression
1024-D vectors are compressed to 128-D, suppressing redundant test-rig noise and isolating discriminative fault features.
Learnable Fusion
The two 128-D vectors combine as shown below, letting the model dynamically prioritize the STFT or CWT branch.
Classification Head
The fused vector passes through Fully Connected layers with Dropout regularization, then a SoftMax layer outputs
probabilities across 24 fault classes.
Zfused = αS ZS + αC ZC
αS and αC are learned weights that set each branch's contribution to the fused representation
Part 1 — Paper Summary

## Slide 9: Validation and Comparison Metrics
RES ULT S
99.38%
Validation Accuracy
0.0183
Validation Loss
0.9946
Precision
0.9938
Recall
0.9932
F1-score
0.9937
MCC
Robustness: high precision and recall together indicate the model is not simply guessing — errors are low and balanced across both false positives and false negatives.
THE L IMITATION
Performance is heavily dependent on specific datasets (IMS, CWRU) recorded under controlled lab conditions. They lack the complexity of real-world scenarios, making
generalization to varying operating contexts a major challenge — though the authors' own experimented data training , suggest transfer learning may help generalize.
Part 1 — Paper Summary

## Slide 10: h
hh
P A R T T W O
Doubts
Open technical questions raised while reviewing the paper

## Slide 11: Doubts Regarding Computation & Discrete Classification
OP EN Q UES T I ON S
1 · Computational Overhead vs. Phase Retention
Converting 1D temporal signals into 224×224 RGB images requires 6.63 GFLOPs of computation and permanently discards non-linear phase information.
DOUBT How does the model compensate for the absence of phase dynamics — and is this compute requirement truly viable for edge-deployed condition monitoring? ( also for reducing computational cost restent last layer has been removed )
2 · Operating Context & Discrete Limits
Real-world industrial machinery operates on a continuous spectrum, yet the SoftMax layer forces predictions into exactly 24 discrete classes.
DOUBT How does the classification head react to an unseen intermediate operating state (e.g. 1500 r/min at 3.0 kN)? Does it risk forcing a false positive onto the
nearest known class?
Part 2 — Doubts & Vulnerabilities

## Slide 12: Doubts Regarding Latent Space Entanglement
OP EN Q UES T I ON S
Domain Shift Susceptibility
The dual backbones compress inputs into a fused 128-D latent vector without any explicit disentanglement constraint — such as an orthogonal or adversarial loss — to separate the sources of variation.
Memorizing Nuisance Data
Deep CNNs are highly prone to memorizing the specific acoustic baseline and operating context of the training test-rig, rather than learning pure structural fault physics.
THE CORE DOUBT
Without forcing the model to separate structural health from RPM / load, how susceptible is this latent representation to loa d and RPM shift?
Part 2 — Doubts & Vulnerabilities

## Slide 13
P A R T T H R E E
Proposed Architecture
A disentangled, physics-guided approach to operating-condition-invariant fault detection

## Slide 14: Defining True Machine Health
T HE CAS E FOR A N EW AP P ROACH
01
The Flaw in Current Models
Most papers focus only on classifying known faults — matching signals to a specific defect — but fail to define general “machine health” robustness.
02
The CBM Priority
In Condition-Based Monitoring, the first step must be distinguishing strictly between “Healthy” and “Degradation” states, with high precision and efficiency.
03
The Environmental Hurdle
Unpredictable environmental noise and variable operating conditions (load / RPM) make generalization nearly impossible; standard filters cannot handle random noise variation.
04
Part 3 — Proposed Architecture
Our Objective
Focus on controlling the operating-condition variable — making the model's prediction invariant to changes in load and RPM.
Scope note: full environmental-noise robustness is treated as out of scope for now — this proposal targets the load / RPM invariance sub-problem specifically.

## Slide 15: The Embedding Problem & Spectrum Smearing
P ROB LEM DI AG N OS I S
The “Black Box” Approach
Current deep learning models treat embedding creation as a black box — letting the network arbitrarily redistribute weights to extract features from STFT / CWT and forcing predictions into 24 discrete classes.
The Flaw of STFT
Changing RPM or load completely redistributes STFT frequency bins and shifts the entire spectrum — proof that simple data-driven feature extraction is highly unstable.
THE GOAL
Design an architecture that dictates exactly what the model extracts — creating a latent space where the Health Vector (Zh) is isolated from Nuisance Information.
Part 3 — Proposed Architecture

## Slide 16: Dual-Latent Space: Disentangling Zh and Zc
P ROP OS ED ARCHI T ECT UR E
Orthogonal Disentanglement
The encoder outputs two explicit vectors — a Health Vector (Zh) and an Operating-Condition Vector (Zc) — separated by an orthogonal constraint, Zh ⊥ Zc.
The RPM / Amplitude Caveat
Operating data cannot simply be deleted. RMS energy, harmonics, and resonance are heavily dependent on RPM — the
model must preserve this physical relationship, not discard it.
Intelligent Fusion
Classification relies on a fusion function that uses the isolated operating data (Zc) to accurately scale and interpret the
structural health data (Zh), shown below. ( THIS I USED FROM DISCNET FUSION AS JUST AN EXMPLE ,)
Zfused = αh Zh + αc Zc (subject to Zh ⊥ Zc)
Part 3 — Proposed Architecture

## Slide 17: Physical Preprocessing: Order Tracking & Envelope Analysis
S I G N AL P ROCES S I N G
STEP 1
Computed Order Tracking
Tachometer data samples the signal relative to shaft angular position — transforming variable frequencies into constant “orders,” solving harmonic scaling and eliminating frequency smearing.
→
STEP 2
Envelope Analysis
Applied alongside COT, this demodulates high-frequency resonant responses from repeating structural impacts (e.g. roller impacts on a crack), isolating the low-frequency repetition rate from noise.
→
STEP 3
Targeted Embedding
These preprocessing constraints ensure the Health Vector (Zh) focuses precisely on true structural damage rather than operating-speed illusions.
Part 3 — Proposed Architecture

## Slide 18: Physics-Guided Loss Functions
T RAI N I N G S T RAT EG Y
CONSTRAINT 1
Predictable Noise Filtration
Zh will be governed by physics-based constraints within the loss function itself — including spectral envelopes for specific fault frequencies (e.g. BPFO, ball-pass frequency of the outer race).
CONSTRAINT 2
Transient Energy Loss
We will experiment with custom loss functions that force a 1D network to focus on transient impacts and energy distribution — capturing the benefits of STFT / CWT without the computational bloat of full 2D image conversion.
Part 3 — Proposed Architecture

## Slide 19: Validation & Next Steps
ROADMAP
01
Research Focus
Extensive parallel experimentation to find the optimal embedding method for extracting and fusing Zh and Zc.
02
Architectural Development
Formulating the exact mathematical loss functions for Zh ⊥ Zc
Designing the fusion architecture for physics-based (Zh) and data-driven (Zc) embeddings
Defining signal-processing constraints for bearing fault frequencies directly in the loss landscape
A VERY IMPORTANT POINT EVERY PROPESED ARCHI IS JUST FOR A IDEA NOTHING IS RIGID AND I AM VERY HAPPY TO GET THE SUGGESTION AND GUIDANCE BY YOU ALL.
03
Part 3 — Proposed Architecture
Benchmark Validation
Testing this framework across top benchmark datasets that feature heavily varying RPM and load conditions, to prove cross-domain robustness.

## Slide 20: Thank you
F O R D I S C U S S I O N
Open questions on compute cost, phase-information loss, discrete-class limits, and latent-space entanglement remain
for the group to weigh in on.
PLEASE CRITIC THE FLAWS .I AM INTRESTED IN FINDING THE SOLUTION OF THESE KIND OF PROBLEM BUT DUE TO LACK OF ENOUGH KNOWLEDGE OF THIIS DOMAIN I AM HEAVILY CONSTRAINED IN SOLVING IT .